## Slide 1: Communication Systems

## Slide 2: History of Communications
Year | Event
1838 | Telegraphy (Morse)
1876 | Telephone (Bell)
1902 | Radio transmission (Marconi)
1933 | FM radio
1936 | TV broadcasting
1953 | Color TV

## Slide 3: History of Communications
Year | Event
1962 | Satellite communication
1972 | Cellular phone
1985 | Fax machines
1990s | GPS, HDTV, handheld computers

## Slide 4: Communication Systems
A communication system conveys information from its source to a destination.
Examples:
  Telephone
  TV
  Radio
  Cell phone
  PDA
  Satellite

## Slide 5: Communication Systems
A communication system is composed of the following:
Input
Transducer
Transmitter
Channel
Receiver
Output
Transducer
Source

## Slide 6: Input Transducer
Source: Analog or digital
Example: Speech, music, written text
Input Transducer: Converts the message produced by a source to a form suitable for the communication system.
Example:
Speech wavesMicrophoneVoltage

## Slide 7: Transmitter
Couple the message to the channel
Operations: Amplification, Modulation
Modulation encodes message into amplitude, phase or frequency of carrier signal (AM, PM, FM)
Advantages:
  Reduce noise and interference
  Multiplexing
  Channel Assignment
Examples: TV station, radio station, web server

## Slide 8: Channel
Physical medium that does the transmission
Examples: Air, wires, coaxial cable, radio wave, laser beam, fiber optic cable
Every channel introduces some amount of distortion, noise and interference

## Slide 9: Receiver
Extracts message from the received signal
Operations: Amplification, Demodulation, Filtering
Goal: The receiver output is a scaled, possibly delayed version of the message signal (ideal transmission)
Examples: TV set, radio, web client

## Slide 10: Output Transducer
Converts electrical signal into the form desired by the system
Examples: Loudspeakers, PC

## Slide 11: Capacity of a Channel
The most important question for a communication channel is the maximum rate at which it can transfer information.
There is a theoretical maximum rate at which information passes error free over the channel, called the channel capacity C.
The famous Hartley-Shannon Law states that the channel capacity C is given by:
C=B*log(1+(S/N)) b/s
where B is the bandwidth, S/N is the signal-to-noise ratio.

## Slide 12: Fundamental Limitations
Therefore, there are two factors that determine the capacity of a channel:
  Bandwidth
  Noise

## Slide 13: Frequency Spectrum
Most precious resource in communications is “frequency spectrum”
The “frequency spectrum” has to be shared by a large number of users and applications:
AM Radio, FM Radio, TV, cellular telephony, wireless local-area-networks, satellite, air traffic control

## Slide 14: Frequency Spectrum
The frequency spectrum has to be managed for a particular physical medium
The spectrum for “over-the-air” communications is allocated by international communications organization
International Telecommunications Union (ITU)
Bangladesh Telecommunication Regulatory Commission (BTRC) designates and licenses frequency bands in the Bangladesh.

## Slide 15: Frequency Spectrum Example
Application | Frequency Band
AM Radio | 0.54-1.6 MHz
TV (Channels 2-6) | 54-88 MHz
FM Radio | 88-108 MHz
TV (Channels 7-13) | 174-216 MHz
Cellular mobile radio | 806-901 MHz

## Slide 16: Noise
Internal and External Noise
Internal Noise: Generated by components within a communication system (thermal noise)
External Noise:
  Atmospheric noise (electrical discharges)
  Man-made noise (ignition noise)
  Interference (multiple transmission paths)