## Slide 1: Introduction to Information Theory

## Slide 2: Father of Digital Communication
The roots of modern digital communication stem from the ground-breaking paper “A Mathematical Theory of Communication” by Claude Elwood Shannon in 1948.

## Slide 3: Model of a Digital Communication System
Destination
Decoding
Communication
Channel
Coding
Information
Source
Message
e.g. English symbols
Encoder
e.g. English to 0,1 sequence
Can have noise
or distortion
Decoder
e.g. 0,1 sequence to English

## Slide 4: Communication Channel Includes

## Slide 5: And even this…

## Slide 6: Shannon’s Definition of Communication
“The fundamental problem of communication is that of reproducing at one point either exactly or approximately a message selected at another point.”
“Frequently the messages have meaning”
“... [which is] irrelevant to the engineering problem.”

## Slide 7: Shannon Wants to…
Shannon wants to find a way for “reliably” transmitting data throughout the channel at “maximal” possible rate.
For example, maximizing the speed of ADSL @ your home
Destination
Decoding
Communication
Channel
Coding
Information
Source

## Slide 8: And he thought about this problem for a while…
He later on found a solution and published in this 1948 paper.

## Slide 9
In his 1948 paper he build a rich theory to the problem of reliable communication, now called “Information Theory” or “The Shannon Theory” in honor of him.

## Slide 10: Shannon’s Vision
Data
Source
Encoding
Channel
Source Decoding
User
Channel Encoding
Channel Decoding

## Slide 11: Example: Disk Storage
Data
Zip
Channel
Unzip
User
Add CRC
Verify CRC

## Slide 12: In terms of Information Theory Terminology
Zip
Source
Encoding
=
Data Compression
Add CRC
Channel Encoding
=
Unzip
Source Decoding
=
Verify CRC
Channel Decoding
=
Data Decompression
Error Protection
Error Correction

## Slide 13: Example: VCD and DVD
Moive
MPEG
Encoder
CD/DVD
MPEG Decoder
TV
RS Encoding
RS Decoding
RS stands for Reed-Solomon Code.

## Slide 14: Example: Cellular Phone
Speech Encoding
Channel
Speech Decoding
CC Encoding
CC Decoding
CC stands for Convolutional Code.
GSM/CDMA

## Slide 15: Example: WLAN IEEE 802.11b
Data
Zip
Channel
Unzip
User
CC Encoding
CC Decoding
CC stands for Convolutional Code.
IEEE 802.11b

## Slide 16: Shannon Theory
The original 1948 Shannon Theory contains:
  Measurement of Information
  Source Coding Theory
  Channel Coding Theory

## Slide 17: Measurement of Information
Shannon’s first question is
“How to measure information
in terms of bits?”
= ? bits
= ? bits

## Slide 18: Or Lottery!?
= ? bits

## Slide 19: Or this…
= ? bits
= ? bits

## Slide 20: All events are probabilistic!
Using Probability Theory, Shannon showed that there is only one way to measure information in terms of number of bits:
called the entropy function

## Slide 21: For example
Tossing a dice:
  Outcomes are 1,2,3,4,5,6
  Each occurs at probability 1/6
  Information provided by tossing a dice is

## Slide 22: Wait! It is nonsense!
The number 2.585-bits is not an integer!!
What does you mean?

## Slide 23: Shannon’s First Source Coding Theorem
Shannon showed:
“To reliably store the information generated by some random source X, you need no more/less than, on the average, H(X) bits for each outcome.”

## Slide 24: Meaning:
If I toss a dice 1,000,000 times and record values from each trial
1,3,4,6,2,5,2,4,5,2,4,5,6,1,….
In principle, I need 3 bits for storing each outcome as 3 bits covers 1-8. So I need 3,000,000 bits for storing the information.
Using ASCII representation, computer needs 8 bits=1 byte for storing each outcome
The resulting file has size 8,000,000 bits

## Slide 25: But Shannon said:
You only need 2.585 bits for storing each outcome.
So, the file can be compressed to yield size
2.585x1,000,000=2,585,000 bits
Optimal Compression Ratio is:

## Slide 26: Let’s Do Some Test!
 | File Size | Compression Ratio
No Compression | 8,000,000 bits | 100%
Shannon | 2,585,000 bits | 32.31%
Winzip | 2,930,736 bits | 36.63%
WinRAR | 2,859,336 bits | 35.74%

## Slide 27: The Winner is
I had mathematically claimed my victory 50 years ago!

## Slide 28: Follow-up Story
Later in 1952, David Huffman,
while was a graduate student in
MIT, presented a systematic
method to achieve the optimal
compression ratio guaranteed by
Shannon. The coding technique is therefore called “Huffman code” in honor of his achievement. Huffman codes are used in nearly every application that involves the compression and transmission of digital data, such as fax machines, modems, computer networks, and high-definition television (HDTV), to name a few.
(1925-1999)

## Slide 29: So far… but how about?
Data
Source
Encoding
Channel
Source Decoding
User
Channel Encoding
Channel Decoding
Done
How?

## Slide 30: The Simplest Case: Computer Network
Communications over computer network, ex. Internet
The major channel impairment herein is
Packet Loss

## Slide 31: Binary Erasure Channel
Impairment like “packet loss” can be viewed as Erasures. Data that are erased mean they are lost during transmission…
0
1
0
1
Erasure
1-p
1-p
p
p
p is the packet loss rate in this network

## Slide 32
Once a binary symbol is erased,
it can not be recovered…
Ex:
  Say, Alice sends 0,1,0,1,0,0 to Bob
  But the network was so poor that Bob only received 0,?,0,?,0,0
  So, Bob asked Alice to send again
  Only this time he received 0,?,?,1,0,0
  and Bob goes CRAZY!
  What can Alice do?
  What if Alice sends
  0000,1111,0000,1111,0000,0000
  Repeating each transmission four times!

## Slide 33: What Good Can This Serve?
Now Alice sends 0000,1111,0000,1111,0000,0000
The only cases Bob can not read Alice are for example
????,1111,0000,1111,0000,0000
all the four symbols are erased.
But this happens at probability p4

## Slide 34
Thus if the original network has packet loss rate p=0.25, by repeating each symbol 4 times, the resulting system has packet loss rate p4=0.00390625
But if the data rate in the original network is 8M bits per second
8Mbps
8Mbps
X 4
2 Mbps
With repetition, Alice can only transmit at 2 M bps
p=0.25
p=0.00390625
Bob
Bob
Alice
Alice

## Slide 35: Shannon challenged:
Is repetition the best Alice can do?

## Slide 36: And he thinks again…

## Slide 37: Shannon’s Channel Coding Theorem
Shannon answered:
“Give me a channel and I can compute a quantity called capacity, C for that channel. Then reliable communication is possible only if your data rate stays below C.”

## Slide 38: What does Shannon mean?
?
?
?
?

## Slide 39: Shannon means
In this example:
8Mbps
p=0.25
He calculated the channel capacity
C=1-p=0.75
And there exists coding scheme such that:
8Mbps
?
8 x (1-p)
=6 Mbps
p=0
Alice
Bob
Alice
Bob

## Slide 40: Unfortunately…
I do not know exactly HOW?
Neither do we… 

## Slide 41: But With 50 Years of Hard Work
We have discovered a lot of good codes:
  Hamming codes
  Convolutional codes,
  Concatenated codes,
  Low density parity check (LDPC) codes
  Reed-Muller codes
  Reed-Solomon codes,
  BCH codes,
  Finite Geometry codes,
  Cyclic codes,
  Golay codes,
  Goppa codes
  Algebraic Geometry codes,
  Turbo codes
  Zig-Zag codes,
  Accumulate codes and Product-accumulate codes,
  …
We now come very close to the dream Shannon had 50 years ago! 

## Slide 42: Nowadays…
Source Coding Theorem has applied to
Channel Coding Theorem has applied to
Image
Compression
Data
Compression
Audio/Video
Compression
Audio
Compression
MPEG
MP3
VCD/DVD – Reed-Solomon Codes
Wireless Communication – Convolutional Codes
Optical Communication – Reed-Solomon Codes
Computer Network – LT codes, Raptor Codes
Space Communication

## Slide 43: Shannon Theory also Enables Space Communication
In 1965, Mariner 4:
Frequency =2.3GHz (S Band)
Data Rate= 8.33 bps
No Source Coding
Repetition code (2 x)
In 2004, Mars Exploration Rovers:
Frequency =8.4 GHz (X Band)
Data Rate= 168K bps
12:1 lossy ICER compression
Concatenated Code

## Slide 44: In 2006, Mars Reconnaissance Orbiter
Frequency =8.4 GHz (X Band)
Data Rate= 12 M bps
2:1 lossless FELICS compression
(8920,1/6) Turbo Code
At Distance 2.15 x 108 Km
Communicates
Faster than

## Slide 45: And Information Theory has Applied to
All kinds of Communications,
Stock Market, Economics
Game Theory and Gambling,
Quantum Physics,
Cryptography,
Biology and Genetics,
and many more…